## Slide 1: Computer Networks
Mayank Pandey
Network Layer

## Slide 2: Two Key Network-Layer Functions
forwarding: move packets from router’s input to appropriate router output
routing: determine route taken by packets from source to dest.
  routing algorithms
analogy:
routing: process of planning trip from source to dest
forwarding: process of getting through single interchange

## Slide 3: IP datagram format
ver
length
32 bits
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
32 bit source IP address
IP protocol version
number
header length
(bytes)
max number
remaining hops
(decremented at
each router)
for
fragmentation/
reassembly
total datagram
length (bytes)
upper layer protocol
to deliver payload to
head.
len
type of
service
“type” of data
flgs
fragment
offset
upper
layer
32 bit destination IP address
Options (if any)
E.g. timestamp,
record route
taken, specify
list of routers
to visit.
how much overhead with TCP?
20 bytes of TCP
20 bytes of IP
= 40 bytes + app layer overhead

## Slide 4: IP Fragmentation & Reassembly
network links have MTU (max.transfer size) - largest possible link-level frame.
  different link types, different MTUs
large IP datagram divided (“fragmented”) within net
  one datagram becomes several datagrams
  “reassembled” only at final destination
  IP header bits used to identify, order related fragments
fragmentation:
in: one large datagram
out: 3 smaller datagrams
reassembly

## Slide 5: IP Fragmentation and Reassembly
ID
=x
offset
=0
fragflag
=0
length
=4000
ID
=x
offset
=0
fragflag
=1
length
=1500
ID
=x
offset
=185
fragflag
=1
length
=1500
ID
=x
offset
=370
fragflag
=0
length
=1040
One large datagram becomes
several smaller datagrams
Example
4000 byte datagram
MTU = 1500 bytes
1480 bytes in data field
offset =
1480/8

## Slide 6: IP addresses: how to get one?
Q: How does a host get IP address?
hard-coded by system admin in a file
  Windows: control-panel->network->configuration->tcp/ip->properties
  UNIX: /etc/rc.config
DHCP: Dynamic Host Configuration Protocol: dynamically get address from as server
  “plug-and-play”

## Slide 7: DHCP: Dynamic Host Configuration Protocol
Goal: allow host to dynamically obtain its IP address from network server when it joins network
  Can renew its lease on address in use
  Allows reuse of addresses (only hold address while connected)
  Support for mobile users who want to join network
DHCP overview:
  host broadcasts “DHCP discover” msg [optional]
  DHCP server responds with “DHCP offer” msg [optional]
  host requests IP address: “DHCP request” msg
  DHCP server sends address: “DHCP ack” msg

## Slide 8: DHCP client-server scenario
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A
B
E
DHCP
server
arriving DHCP
client needs
address in this
network

## Slide 9: DHCP client-server scenario
DHCP server: 223.1.2.5
arriving
client
time
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 654
Lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddrr: 223.1.2.4
transaction ID: 655
Lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 655
Lifetime: 3600 secs

## Slide 10: DHCP: more than IP address
DHCP can return more than just allocated IP address on subnet:
  address of first-hop router for client
  name and IP address of DNS sever
  network mask (indicating network versus host portion of address)

## Slide 11: DHCP: example
connecting laptop needs its IP address, addr of first-hop router, addr of DNS server: use DHCP
router
(runs DHCP)
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in 802.1 Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet demuxed to IP demuxed, UDP demuxed to DHCP
168.1.1.1

## Slide 12: DHCP: example
DCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server
router
(runs DHCP)
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
encapsulation of DHCP server, frame forwarded to client, demuxing up to DHCP at client
client now knows its IP address, name and IP address of DSN server, IP address of its first-hop router

## Slide 13: IP addresses: how to get one?
Q: How does network get subnet part of IP addr?
A: gets allocated portion of its provider ISP’s address space
ISP's block 11001000 00010111 00010000 00000000 200.23.16.0/20
Organization 0 11001000 00010111 00010000 00000000 200.23.16.0/23
Organization 1 11001000 00010111 00010010 00000000 200.23.18.0/23
Organization 2 11001000 00010111 00010100 00000000 200.23.20.0/23
... ….. …. ….
Organization 7 11001000 00010111 00011110 00000000 200.23.30.0/23

## Slide 14: Hierarchical addressing: route aggregation
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning
199.31.0.0/16”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
Hierarchical addressing allows efficient advertisement of routing
information:

## Slide 15: Hierarchical addressing: more specific routes
ISPs-R-Us has a more specific route to Organization 1
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning 199.31.0.0/16
or 200.23.18.0/23”
200.23.20.0/23
Organization 2
.
.
.
.
.
.

## Slide 16: IP addressing: the last word...
Q: How does an ISP get block of addresses?
A: ICANN: Internet Corporation for Assigned
Names and Numbers
  allocates addresses
  manages DNS
  assigns domain names, resolves disputes

## Slide 17: NAT: Network Address Translation
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
138.76.29.7
local network
(e.g., home network)
10.0.0/24
rest of
Internet
Datagrams with source or
destination in this network
have 10.0.0/24 address for
source, destination (as usual)
All datagrams leaving local
network have same single source NAT IP address: 138.76.29.7,
different source port numbers

## Slide 18: NAT: Network Address Translation
Motivation: local network uses just one IP address as far as outside world is concerned:
  range of addresses not needed from ISP: just one IP address for all devices
  can change addresses of devices in local network without notifying outside world
  can change ISP without changing addresses of devices in local network
  devices inside local net not explicitly addressable, visible by outside world (a security plus).

## Slide 19: NAT: Network Address Translation
Implementation: NAT router must:
  outgoing datagrams: replace (source IP address, port #) of every outgoing datagram to (NAT IP address, new port #)
    . . . remote clients/servers will respond using (NAT IP address, new port #) as destination addr.
  remember (in NAT translation table) every (source IP address, port #) to (NAT IP address, new port #) translation pair
  incoming datagrams: replace (NAT IP address, new port #) in dest fields of every incoming datagram with corresponding (source IP address, port #) stored in NAT table

## Slide 20: NAT: Network Address Translation
10.0.0.1
10.0.0.2
10.0.0.3
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
10.0.0.4
138.76.29.7
1: host 10.0.0.1
sends datagram to
128.119.40.186, 80
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router
changes datagram
source addr from
10.0.0.1, 3345 to
138.76.29.7, 5001,
updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: Reply arrives
dest. address:
138.76.29.7, 5001
4: NAT router
changes datagram
dest addr from
138.76.29.7, 5001 to 10.0.0.1, 3345

## Slide 21: NAT: Network Address Translation
16-bit port-number field:
  60,000 simultaneous connections with a single LAN-side address!
NAT is controversial:
  routers should only process up to layer 3
  violates end-to-end argument
    NAT possibility must be taken into account by app designers, e.g., P2P applications
  address shortage should instead be solved by IPv6

## Slide 22: ICMP: Internet Control Message Protocol
used by hosts & routers to communicate network-level information
  error reporting: unreachable host, network, port, protocol
  echo request/reply (used by ping)
network-layer “above” IP:
  ICMP msgs carried in IP datagrams
ICMP message: type, code plus first 8 bytes of IP datagram causing error
Type Code description
0 0 echo reply (ping)
3 0 dest. network unreachable
3 1 dest host unreachable
3 2 dest protocol unreachable
3 3 dest port unreachable
3 6 dest network unknown
3 7 dest host unknown
4 0 source quench (congestion
control - not used)
8 0 echo request (ping)
9 0 route advertisement
10 0 router discovery
11 0 TTL expired
12 0 bad IP header

## Slide 23: Traceroute and ICMP
Source sends series of UDP segments to dest
  first has TTL =1
  second has TTL=2, etc.
  unlikely port number
When nth datagram arrives to nth router:
  router discards datagram
  and sends to source an ICMP message (type 11, code 0)
  ICMP message includes name of router & IP address
when ICMP message arrives, source calculates RTT
traceroute does this 3 times
Stopping criterion
UDP segment eventually arrives at destination host
destination returns ICMP “port unreachable” packet (type 3, code 3)
when source gets this ICMP, stops.

## Slide 24: IPv6
Initial motivation: 32-bit address space soon to be completely allocated.
Additional motivation:
  header format helps speed processing/forwarding
  header changes to facilitate QoS
  IPv6 datagram format:
  fixed-length 40 byte header
  no fragmentation allowed

## Slide 25: IPv6 Header (Cont)
Priority: identify priority among datagrams in flow
Flow Label: identify datagrams in same “flow.”
(concept of“flow” not well defined).
Next header: identify upper layer protocol for data
data
destination address
(128 bits)
source address
(128 bits)
payload len
next hdr
hop limit
flow label
pri
ver
32 bits

## Slide 26: Other Changes from IPv4
Checksum: removed entirely to reduce processing time at each hop
Options: allowed, but outside of header, indicated by “Next Header” field
ICMPv6: new version of ICMP
  additional message types, e.g. “Packet Too Big”
  multicast group management functions

## Slide 27: Transition From IPv4 To IPv6
Not all routers can be upgraded simultaneous
  no “flag days”
  How will the network operate with mixed IPv4 and IPv6 routers?
Tunneling: IPv6 carried as payload in IPv4 datagram among IPv4 routers

## Slide 28: Tunneling
A
B
E
F
IPv6
IPv6
IPv6
IPv6
tunnel
Logical view:
Physical view:
A
B
E
F
IPv6
IPv6
IPv6
IPv6
IPv4
IPv4

## Slide 29: Tunneling
A
B
E
F
IPv6
IPv6
IPv6
IPv6
tunnel
Logical view:
Physical view:
A
B
E
F
IPv6
IPv6
IPv6
IPv6
C
D
IPv4
IPv4
Flow: X
Src: A
Dest: F
data
Flow: X
Src: A
Dest: F
data
Flow: X
Src: A
Dest: F
data
Src:B
Dest: E
Flow: X
Src: A
Dest: F
data
Src:B
Dest: E
A-to-B:
IPv6
E-to-F:
IPv6
B-to-C:
IPv6 inside
IPv4
B-to-C:
IPv6 inside
IPv4

## Slide 30: Graph abstraction
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
Graph: G = (N,E)
N = set of routers = { u, v, w, x, y, z }
E = set of links ={ (u,v), (u,x), (v,x), (v,w), (x,w), (x,y), (w,y), (w,z), (y,z) }
Remark: Graph abstraction is useful in other network contexts
Example: P2P, where N is set of peers and E is set of TCP connections

## Slide 31: Graph abstraction: costs
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
c(x,x’) = cost of link (x,x’)
- e.g., c(w,z) = 5
cost could always be 1, or
inversely related to bandwidth,
or inversely related to
congestion
Cost of path (x1, x2, x3,…, xp) = c(x1,x2) + c(x2,x3) + … + c(xp-1,xp)
Question: What’s the least-cost path between u and z ?
Routing algorithm: algorithm that finds least-cost path

## Slide 32: Routing Algorithm classification
Global or decentralized information?
Global:
all routers have complete topology, link cost info
“link state” algorithms
Decentralized:
router knows physically-connected neighbors, link costs to neighbors
iterative process of computation, exchange of info with neighbors
“distance vector” algorithms
Static or dynamic?
Static:
routes change slowly over time
Dynamic:
routes change more quickly
  periodic update
  in response to link cost changes

## Slide 33: A Link-State Routing Algorithm
Dijkstra’s algorithm
net topology, link costs known to all nodes
  accomplished via “link state broadcast”
  all nodes have same info
computes least cost paths from one node (‘source”) to all other nodes
  gives forwarding table for that node
iterative: after k iterations, know least cost path to k dest.’s
Notation:
c(x,y): link cost from node x to y; = ∞ if not direct neighbors
D(v): current value of cost of path from source to dest. v
p(v): predecessor node along path from source to v
N': set of nodes whose least cost path definitively known

## Slide 34: Dijsktra’s Algorithm
1 Initialization:
2 N' = {u}
3 for all nodes v
4 if v adjacent to u
5 then D(v) = c(u,v)
6 else D(v) = ∞
7
8 Loop
9 find w not in N' such that D(w) is a minimum
10 add w to N'
11 update D(v) for all v adjacent to w and not in N' :
12 D(v) = min( D(v), D(w) + c(w,v) )
13 /* new cost to v is either old cost to v or known
14 shortest path cost to w plus cost from w to v */
15 until all nodes in N'

## Slide 35
w
3
4
v
x
u
5
3
7
4
y
8
z
2
7
9
Dijkstra’s algorithm: example
Step
N'
D(v)
p(v)
0
1
2
3
4
5
D(w)
p(w)
D(x)
p(x)
D(y)
p(y)
D(z)
p(z)
u
∞
∞
7,u
3,u
5,u
uw
∞
11,w
6,w
5,u
14,x
11,w
6,w
uwx
uwxv
14,x
10,v
uwxvy
12,y
Notes:
construct shortest path tree by tracing predecessor nodes
ties can exist (can be broken arbitrarily)
uwxvyz

## Slide 36: Dijkstra’s algorithm: another example
Step
0
1
2
3
4
5
N'
u
ux
uxy
uxyv
uxyvw
uxyvwz
D(v),p(v)
2,u
2,u
2,u
D(w),p(w)
5,u
4,x
3,y
3,y
D(x),p(x)
1,u
D(y),p(y)
∞
2,x
D(z),p(z)
∞
∞
4,y
4,y
4,y
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5

## Slide 37: Dijkstra’s algorithm: example (2)
u
y
x
w
v
z
Resulting shortest-path tree from u:
v
x
y
w
z
(u,v)
(u,x)
(u,x)
(u,x)
(u,x)
destination
link
Resulting forwarding table in u:

## Slide 38: Distance Vector Algorithm
Bellman-Ford Equation (dynamic programming)
Define
dx(y) := cost of least-cost path from x to y
Then
dx(y) = min {c(x,v) + dv(y) }
where min is taken over all neighbors v of x
v

## Slide 39: Bellman-Ford example
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
Clearly, dv(z) = 5, dx(z) = 3, dw(z) = 3
du(z) = min { c(u,v) + dv(z),
c(u,x) + dx(z),
c(u,w) + dw(z) }
= min {2 + 5,
1 + 3,
5 + 3} = 4
Node that achieves minimum is next
hop in shortest path ➜ forwarding table
B-F equation says:

## Slide 40: Distance Vector Algorithm
Dx(y) = estimate of least cost from x to y
  x maintains distance vector Dx = [Dx(y): y є N ]
node x:
  knows cost to each neighbor v: c(x,v)
  maintains its neighbors’ distance vectors. For each neighbor v, x maintains Dv = [Dv(y): y є N ]

## Slide 41: Distance vector algorithm (4)
Basic idea:
from time-to-time, each node sends its own distance vector estimate to neighbors
when x receives new DV estimate from neighbor, it updates its own DV using B-F equation:
Dx(y) ← minv{c(x,v) + Dv(y)} for each node y ∊ N
under minor, natural conditions, the estimate Dx(y) converge to the actual least cost dx(y)

## Slide 42: Distance Vector Algorithm (5)
Iterative, asynchronous: each local iteration caused by:
local link cost change
DV update message from neighbor
Distributed:
each node notifies neighbors only when its DV changes
  neighbors then notify their neighbors if necessary
wait for (change in local link cost or msg from neighbor)
recompute estimates
if DV to any dest has changed, notify neighbors
Each node:

## Slide 43
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0
from
cost to
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
∞
∞
∞
7
1
0
cost to
∞
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
time
x
z
1
2
7
y
node x table
node y table
node z table
Dx(y) = min{c(x,y) + Dy(y), c(x,z) + Dz(y)} = min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) + Dy(z), c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3
3
2

## Slide 44
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
0 2 7
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 7
from
cost to
x y z
x
y
z
∞
∞
∞
7
1
0
cost to
∞
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
2 0 1
7 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
time
x
z
1
2
7
y
node x table
node y table
node z table
Dx(y) = min{c(x,y) + Dy(y), c(x,z) + Dz(y)} = min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) + Dy(z), c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3

## Slide 45: Distance Vector: link cost changes
Link cost changes:
node detects local link cost change
updates routing info, recalculates distance vector
if DV changes, notify neighbors
“good
news
travels
fast”
x
z
1
4
50
y
1
t0 : y detects link-cost change, updates its DV, informs its neighbors.
t1 : z receives update from y, updates its table, computes new least cost to x , sends its neighbors its DV.
t2 : y receives z’s update, updates its distance table. y’s least costs do not change, so y does not send a message to z.

## Slide 46: Distance Vector: link cost changes
Link cost changes:
good news travels fast
bad news travels slow - “count to infinity” problem!
44 iterations before algorithm stabilizes
Poisoned reverse:
If Z routes through Y to get to X :
  Z tells Y its (Z’s) distance to X is infinite (so Y won’t route to X via Z)
will this completely solve count to infinity problem?
x
z
1
4
50
y
60

## Slide 47: Comparison of LS and DV algorithms
Message complexity
LS: with n nodes, E links, O(nE) msgs sent
DV: exchange between neighbors only
  convergence time varies
Speed of Convergence
LS: O(n2) algorithm requires O(nE) msgs
  may have oscillations
DV: convergence time varies
  may be routing loops
  count-to-infinity problem
Robustness: what happens if router malfunctions?
LS:
  node can advertise incorrect link cost
  each node computes only its own table
DV:
  DV node can advertise incorrect path cost
  each node’s table used by others
    error propagate thru network

## Slide 48: Hierarchical Routing
scale: with 200 million destinations:
can’t store all dest’s in routing tables!
routing table exchange would swamp links!
administrative autonomy
internet = network of networks
each network admin may want to control routing in its own network
Our routing study thus far - idealization
all routers identical
network “flat”
… not true in practice

## Slide 49: Hierarchical Routing
aggregate routers into regions, “autonomous systems” (AS)
routers in same AS run same routing protocol
  “intra-AS” routing protocol
  routers in different AS can run different intra-AS routing protocol
gateway router
at “edge” of its own AS
has link to router in another AS

## Slide 50: Interconnected ASes
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
Intra-AS
Routing
algorithm
Inter-AS
Routing
algorithm
Forwarding
table
3c
forwarding table configured by both intra- and inter-AS routing algorithm
  intra-AS sets entries for internal dests
  inter-AS & intra-As sets entries for external dests

## Slide 51: Inter-AS tasks
suppose router in AS1 receives datagram destined outside of AS1:
  router should forward packet to gateway router, but which one?
AS1 must:
learn which dests are reachable through AS2, which through AS3
propagate this reachability info to all routers in AS1
job of inter-AS routing!
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks

## Slide 52: Example: Setting forwarding table in router 1d
suppose AS1 learns (via inter-AS protocol) that subnet x reachable via AS3 (gateway 1c) but not via AS2.
  inter-AS protocol propagates reachability info to all internal routers
router 1d determines from intra-AS routing info that its interface I is on the least cost path to 1c.
  installs forwarding table entry (x,I)
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks
x
…

## Slide 53: Example: Choosing among multiple ASes
now suppose AS1 learns from inter-AS protocol that subnet x is reachable from AS3 and from AS2.
to configure forwarding table, router 1d must determine which gateway it should forward packets towards for dest x
  this is also job of inter-AS routing protocol!
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks
x
……
…
?

## Slide 54: Example: Choosing among multiple ASes
Learn from inter-AS
protocol that subnet
x is reachable via
multiple gateways
Use routing info
from intra-AS
protocol to determine
costs of least-cost
paths to each
of the gateways
Hot potato routing:
Choose the gateway
that has the
smallest least cost
Determine from
forwarding table the
interface I that leads
to least-cost gateway.
Enter (x,I) in
forwarding table
now suppose AS1 learns from inter-AS protocol that subnet x is reachable from AS3 and from AS2.
to configure forwarding table, router 1d must determine towards which gateway it should forward packets for dest x.
  this is also job of inter-AS routing protocol!
hot potato routing: send packet towards closest of two routers.

## Slide 55: Intra-AS Routing
also known as Interior Gateway Protocols (IGP)
most common Intra-AS routing protocols:
  RIP: Routing Information Protocol
  OSPF: Open Shortest Path First
  IGRP: Interior Gateway Routing Protocol (Cisco proprietary)

## Slide 56: RIP ( Routing Information Protocol)
included in BSD-UNIX distribution in 1982
distance vector algorithm
  distance metric: # hops (max = 15 hops), each link has cost 1
  DVs exchanged with neighbors every 30 sec in response message (aka advertisement)
  each advertisement: list of up to 25 destination subnets (in IP addressing sense)
D
C
B
A
u
v
w
x
y
z
subnet hops
u 1
v 2
w 2
x 3
y 3
z 2
from router A to destination subnets:

## Slide 57: RIP: Example
destination subnet next router # hops to dest
w A 2
y B 2
z B 7
x -- 1
…. …. ....
routing table in router D
w
x
y
z
A
C
D
B

## Slide 58: RIP: Example
destination subnet next router # hops to dest
w A 2
y B 2
z B 7
x -- 1
…. …. ....
routing table in router D
w
x
y
z
A
C
D
B
A
5
dest next hops
w - 1
x - 1
z C 4
…. … ...
A-to-D advertisement

## Slide 59: RIP: Link Failure and Recovery
If no advertisement heard after 180 sec --> neighbor/link declared dead
  routes via neighbor invalidated
  new advertisements sent to neighbors
  neighbors in turn send out new advertisements (if tables changed)
  link failure info quickly (?) propagates to entire net
  poison reverse used to prevent ping-pong loops (infinite distance = 16 hops)

## Slide 60: RIP Table processing
RIP routing tables managed by application-level process called route-d (daemon)
advertisements sent in UDP packets, periodically repeated
physical
link
network forwarding
(IP) table
Transport
(UDP)
routed
physical
link
network
(IP)
Transprt
(UDP)
routed
forwarding
table

## Slide 61: OSPF (Open Shortest Path First)
“open”: publicly available
uses Link State algorithm
  LS packet dissemination
  topology map at each node
  route computation using Dijkstra’s algorithm
OSPF advertisement carries one entry per neighbor router
advertisements disseminated to entire AS (via flooding)
  carried in OSPF messages directly over IP (rather than TCP or UDP

## Slide 62: OSPF “advanced” features (not in RIP)
security: all OSPF messages authenticated (to prevent malicious intrusion)
multiple same-cost paths allowed (only one path in RIP)
for each link, multiple cost metrics for different TOS (e.g., satellite link cost set “low” for best effort ToS; high for real time ToS)
integrated uni- and multicast support:
  Multicast OSPF (MOSPF) uses same topology data base as OSPF
hierarchical OSPF in large domains.

## Slide 63: Hierarchical OSPF
boundary router
backbone router
Area 1
Area 2
Area 3
backbone
area
border
routers
internal
routers

## Slide 64: Hierarchical OSPF
two-level hierarchy: local area, backbone.
  link-state advertisements only in area
  each nodes has detailed area topology; only know direction (shortest path) to nets in other areas.
area border routers: “summarize” distances to nets in own area, advertise to other Area Border routers.
backbone routers: run OSPF routing limited to backbone.
boundary routers: connect to other AS’s.

## Slide 65: Internet inter-AS routing: BGP
BGP (Border Gateway Protocol): the de facto inter-domain routing protocol
  “glue that holds the Internet together”
BGP provides each AS a means to:
  eBGP: obtain subnet reachability information from neighboring ASs.
  iBGP: propagate reachability information to all AS-internal routers.
  determine “good” routes to other networks based on reachability information and policy.
allows subnet to advertise its existence to rest of Internet: “I am here”

## Slide 66: BGP basics
when AS3 advertises a prefix to AS1:
  AS3 promises it will forward datagrams towards that prefix
  AS3 can aggregate prefixes in its advertisement
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks
BGP session: two BGP routers (“peers”) exchange BGP messages:
  advertising paths to different destination network prefixes (“path vector” protocol)
  exchanged over semi-permanent TCP connections
BGP
message

## Slide 67: BGP basics: distributing path information
AS3
AS2
3b
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks
using eBGP session between 3a and 1c, AS3 sends prefix reachability info to AS1.
  1c can then use iBGP do distribute new prefix info to all routers in AS1
  1b can then re-advertise new reachability info to AS2 over 1b-to-2a eBGP session
when router learns of new prefix, it creates entry for prefix in its forwarding table.
eBGP session
iBGP session

## Slide 68: Path attributes & BGP routes
advertised prefix includes BGP attributes
  prefix + attributes = “route”
two important attributes:
  AS-PATH: contains ASs through which prefix advertisement has passed: e.g., AS 67, AS 17
  NEXT-HOP: indicates specific internal-AS router to next-hop AS. (may be multiple links from current AS to next-hop-AS)
gateway router receiving route advertisement uses import policy to accept/decline
  e.g., never route through AS x
  policy-based routing

## Slide 69: BGP route selection
router may learn about more than 1 route to destination AS, selects route based on:
  local preference value attribute: policy decision
  shortest AS-PATH
  closest NEXT-HOP router: hot potato routing
  additional criteria

## Slide 70: BGP messages
BGP messages exchanged between peers over TCP connection
BGP messages:
  OPEN: opens TCP connection to peer and authenticates sender
  UPDATE: advertises new path (or withdraws old)
  KEEPALIVE: keeps connection alive in absence of UPDATES; also ACKs OPEN request
  NOTIFICATION: reports errors in previous msg; also used to close connection

## Slide 71: BGP routing policy
A,B,C are provider networks
X,W,Y are customer (of provider networks)
X is dual-homed: attached to two networks
  X does not want to route from B via X to C
  .. so X will not advertise to B a route to C
A
B
C
W
X
Y
legend:
customer
network:
provider
network

## Slide 72: BGP routing policy (2)
A advertises path AW to B
B advertises path BAW to X
Should B advertise path BAW to C?
  No way! B gets no “revenue” for routing CBAW since neither W nor C are B’s customers
  B wants to force C to route to w via A
  B wants to route only to/from its customers!
A
B
C
W
X
Y
legend:
customer
network:
provider
network

## Slide 73: Why different Intra- and Inter-AS routing ?
Policy:
Inter-AS: admin wants control over how its traffic routed, who routes through its net.
Intra-AS: single admin, so no policy decisions needed
Scale:
hierarchical routing saves table size, reduced update traffic
Performance:
Intra-AS: can focus on performance
Inter-AS: policy may dominate over performance